LOW Step (Step I)
Mode (1):
_ Position
_ Sound
_ Footprint
_ Marker
_ GPIO
_ GPIO module
_ Variable
_ Sleep
_ Break

ex: (name:__|time_out:__|mode:__|data:__)

Name → name step
time_out → set time out for step if set -1 while infinity
mode → there are 8 mode (1),
data → data to action step. With each mode will have data specific for them.

Position
_x
_y
_z
_w
_mode:
ex:
(name:A|time_out:-1|mode:position|data: x~=0~~y=0~~z=0~~w=1~~mode=normal~)
name:A → step I name is A
time_out:-1 → step I while wait until finish not have timeout
mode:position → step I have mode position.
data: x~=0~~y=0~~z=0~~w=1~~mode=normal~ → data for position mode. X,Y,Z,W target goal for robot. mode is mode operating in position. Mode: (normal/line_follow)

Sound
_music_start
_music_mode
ex:
(name:A|time_out:-1|mode:sound|data:~music_start=1~~music_mode=1~)
name:A → step I name is A
time_out:-1 → step I while wait until finish not have timeout
mode:sound → step I have mode sound.
data:~music_start=1~~music_mode=1~ → data for sound mode. music_start 0/1. If music_start=1 → robot while check music_mode=1/2/3/4 (basic/buzze1/buzze2/custom) to start sound.

Footprint
_x1
_y1
_x2
_y2
ex:
(name:Footprint_default|time_out:-1|mode:footprint|data:~x1=-0.41~~y1=-0.345~~x2=0.41~~y2=0.345~)
 name: Footprint_default → step I name is Footprint_default
time_out:-1 → step I while wait until finish not have timeout
mode: footprint → step I have mode footprint
data:~x1=-0.41~~y1=-0.345~~x2=0.41~~y2=0.345-> data footprint x1 <0 y1<0 x2 >0 y2>0
(0,0) is point center robot. X1,Y,1,X2,Y2 value for footprint set.

Marker
_marker_type
_marker_dir
_off_set_x1
_off_set_y1
_off_set_dis
_off_set_angle
_sx1
_sx2
_sy1
_sy2

ex1:
(name:D_Defaut_1p2|time_out:-1|mode:marker|data:~marker_type=none_marker_dis~~off_set_dis=1.2~~sx1=0.01~~sx2=0.15~~sy1=0~~sy2=0~)

ex2:
(name:Bar_Lift|time_out:-1|mode:marker|data:~marker_type=bar_marker~~marker_dir=front_ward~~off_set_x1=-0.5~~off_set_y1=0~~sx1=0.01~~sx2=0.01~~sy1=0.01~~sy2=0.01~)

sx1,sx2,sy1,sy2 safe from footprint robot have being set. marker_type (vl_marker/l_marker/bar_marker/none_marker_dis/none_marker_angle) chose mode for marker action.
ọther off set see document marker.

GPIO
out_set
out_reset
not_set_out
in_on
in_off
in_pullup
in_pulldown

ex:
(name:A|time_out:-1|mode:gpio|data:~not_set_out=1~~out_set=0~)
(name:B|time_out:-1|mode:gpio|data:~not_set_out=1~~out_set=0~~in_on=1,2,3,4~)

Read and set gpio in robot device .not_set_out=1 while set output, if not_set_out=0 wait for output have been set, not publish topic to set out.

GPIO_module
string name_seri
out_set
out_reset
not_set_out
in_on
in_off
in_pullup
in_pulldown
Read and set gpio out robot device.not_set_out=1 while set output, if not_set_out=0 wait for output have been set, not publish topic to set out. name_seri → chose device to read and set gpio.

Variable
command_action
name_variable
focus_value
ex:
(name:new_variable|time_out:-1|mode:variable|data:~command_action=new~~name_variable=a~~focus_value=0~)
ex2:
(name:a_1|time_out:-1|mode:variable|data:~command_action=equal~~name_variable=a~~focus_value=1~)

command_action→ action with varibale (=,>,… see table).name_variable → what variable robot have to action. focus_value → value variable have to interact.

Talble:
new
equal (=)
equal_as(==)
equal_not(!=)
smaller_as (<)
smaller_equal_as (<=)
bigger_as (>)
bigger_equal_as(>=)
equal_+ (a,b a=a+b)
equal_- (a,b a=a-b)
reset (not need name variable)
delete (not need name variable)
Sleep
time_sleep

ex:
(name:S1|time_out:-1|mode:sleep|data:~time_sleep=1~)

Break

ex: (name:break|time_out:-1|mode:break|data:~~)

Multiple LOW Step (Multiple Step I)

(A)(B)(C)…(D)
A,B,C,D is step_I create by user.
ex:
(name:R_90|time_out:-1|mode:marker|data:~marker_type=none_marker_angle~~off_set_angle=90~~sx1=0.01~~sx2=0.01~~sy1=0.03~~sy2=0.03~)(name:Basic|time_out:-1|mode:sound|data:~music_start=1~~music_mode=3~)(name:HS20_CM1b_II|time_out:-1|mode:position|data:~x=63.16~~y=-0.16~~z=-0.7009092643~~w=0.7132504492~~mode=normal~)(name:Buzzer2|time_out:-1|mode:sound|data:~music_start=1~~music_mode=2~)(name:R_a60|time_out:-1|mode:marker|data:~marker_type=none_marker_angle~~off_set_angle=-60~~sx1=0.03~~sx2=0.03~~sy1=0.03~~sy2=0.03~)